New Sandvik DT922i – the ultimate all-round tunneling jumbo

Sandvik Construction is introducing a completely new tunneling jumbo to its extensive offering: the new, fully automated, DT922i tunneling jumbo. This will bring to customers true tunneling quality, reliability and exceptional versatility. With a new articulated carrier, it features a next generation cabin supplying 25 % increased visibility, and noise level of less than 69 dB at all times. Intelligent, state-of-the-art control system, and Sandvik’s iSURE ® excavation management tool, create a combination which will change the future of tunneling.

The DT922i is a fully-automated electro-hydraulic two-boom tunneling jumbo with a completely new articulated carrier. It offers unique intelligence, true power and ultimate versatility to handle any tunneling job that comes along. Designed to improve the tunneling quality through its novel automation and planning function, the DT922i has been developed for excavating cross sections up to 125m², including face drilling, bolt hole drilling, and long-hole drilling.

“If you want a jumbo that will be able to perform all different tunneling excavation, this is the one for you,” says Tommi Salo, Product Line Manager, Tunneling, Sandvik Construction, who adds:  “Our aim was to create an all-round jumbo that is high in performance, reliable in use and possesses the same intelligence like our other i-series jumbos, but at the same time is able to offer the customer the flexibility they were after in terms of new carrier and improved automation. Looking at the end result, I think we have succeeded very well.”

Maximized versatility

The DT922i comes with many new features that increase productivity simply through the machine’s genuine adaptability to different working sites. The new articulated carrier enables the jumbo to operate in tight tunnels with narrow corners. Moreover, the new optional cabin lifting system gives improved visibility, but at the same time allows to tram in low tunnels. The hydrostatic transmission system and joystick control enables very precise dynamic control of tramming speed and steering. The practical multi-voltage concept for different electric voltages allows easy and fast shift to different working sites. Combined with the efficient RD525 rock drill, intelligent drilling and boom control systems, as well as the iSURE® tunnel management system, the DT922i offers an unbeatable combination for any tunnel excavation.

Advanced drilling and boom control systems

Optimized performance with amplified drilling automation, corner stones for the design of the new tunneling jumbo, has resulted from the use of Sandvik Intelligent Control System Architecture (SICA). This is a well-proven and intelligent drilling control system with nine different hole type settings, and three alternative control methods: manual drilling control, feed percussion follow-up, and intelligent torque control. The DT922i also possesses a new easy-to-use boom control system with three different modes for manual boom control. With this new technology the accuracy of drilling is brought to a completely new level which facilitates enhanced and maximized performance.

Efficient drilling

Equipped with the powerful Sandvik RD525 rock drill which provides 17 % higher penetration rates, 40 % longer tool life for the shank, as well as 17 % for the bits (when compared to its predecessors), the DT922i delivers superb performance in any conditions. Its two accurate SB100i booms are equipped with stiff square shape profile giving maximized support to the rock drills and further add to the precision in drilling.

Operator comfort with modern, ergonomic cabin and state-of-the-art user interface

The DT922i’s brand new cabin comes with improved ergonomics and maximized safety. The new design delivers 25 % greater visibility sector, reduced dust levels and provides more operator space. With noise levels under 69 dB at all times, it thus supplies a comfortable and safe working environment for the operator. Additionally the new state-of-the-art user interface, with touchscreen, is easy to work displaying comprehensive diagnostics with all drilling and carrier parameters split into logical subsystems and shown on one display.

EHS features in-built

Environmental, health and safety issues have not been forgotten in the design of the new DT922i. All lights of the new jumbo are based on LED-technology, which when compared to the more commonly used High Intensity Discharge (HID) lights, have  up to 500 % increased lifetime,  and consume 50 % less energy. In addition, the laser scanner access detection system optimizes personnel safety. The DT922i is available with the fuel efficient and emissions friendly Tier 3 diesel engine (119 kW) as standard, or the optional Tier 4 Final (122 kW), which provides even greater levels of reduced emissions, with the powerpack consisting of two 75kW IE3 compliant electric motors. These being just examples of the new jumbo’s EHS-features, which enable the DT922i to be a trailblazer in modern underground drilling, not just from a productivity perspective but also an EHS one.

Automated drill planning

Two automation levels are also offered: gold and platinum. The standard gold package facilitates drilling according to predefined drill plans. This automation level includes features such as drilling to predefined depth, drill plan visualization, rig navigation and an option for automatic long hole drilling. It also integrates the iSURE® tunnel management tool for creating accurate plans for drilling, charging and blasting, as well as data collection and analysis tool for improving work cycle and process. The enhanced platinum package includes all features from the gold package, but enables full automatic face drilling with “iDATA”.

The new DT922i tunneling jumbo is set to be introduced during the second and third quarters of 2015 at several local customer focused events around the world.

| TECHNICAL SPECIFICATION IN BRIEF | SANDVIK DT922i |
| --- | --- |
| Hydraulic rock drill | Sandvik RD525 |
| Drill feed | Sandvik TF5i (14’ to 20’) |
| Boom | Sandvik SB100i |
| Control system | Sandvik SICA |
| Automation levels | Gold (standard) / Platinum (optional) packages |
| Coverage area | 14 800 x 9 000 mm (125m²) |
| Hole length | Up to 5 880 mm |
| Turning width (T-section) | 5 300 mm |
| Transport / drilling width | 2 500 mm* / 3 500 mm |
| Transport height | 3 190 mm** / 3 590 mm |
| Transport length | 14 990 mm |
| Total weight | 30 000 kg (depending on options) |

*   2 570 mm with THR.

**  Minimum 3 190 mm with cabin lifting system.

For further information please contact:

Katri Miss
Marketing Communications Manager
Surface Drilling and Tunneling
Sandvik Construction
Office Phone: +358 205 44 4029
Mobile: +358 50 3609969
E-mail: katri.miss@sandvik.com

--------------------------------------------------------------------------------------------------------------------------------------------

Sandvik Group
Sandvik is a high-tech and global engineering group offering advanced products and services that enhance customer productivity, profitability and safety.  We have world - leading positions in selected areas - tools for metal cutting, equipment and tools for the mining and construction industries, stainless materials, special alloys, metallic and ceramic resistance materials as well as process systems. In 2014 the Group had about 47,000 employees and representation in approximately 130 countries, with sales of about 89,000 million SEK.

Sandvik Construction
Sandvik Construction is a business area within the Sandvik Group providing solutions for virtually any construction industry application encompassing such diverse businesses as surface rock quarrying, tunneling, excavation, demolition, road building, recycling and civil engineering. The range of products includes rock tools, drilling rigs, breakers, bulk-materials handling and crushing and screening machinery. In 2014 sales were about 9,000 million SEK, with approximately 3,000 employees.