When the level of precision is a question of life and death

Special projects rely on Sandvik DTi jumbos with iSURE®

Sandvik DTi jumbos have gained solid trust with contractors operating in especially demanding projects. Two excellent examples are research projects exploring the possibilities for final repositories of nuclear waste in both Sweden and Finland.

Nuclear waste final repository research projects have very high demands on drilling accuracy and overall quality of the end result. These projects cannot take the risk of any errors or poor quality excavation work. Sandvik DTi jumbos and iSURE tunnel excavation management tool have proved themselves as an excellent choice.

Nuclear waste repository research in Sweden and Finland

In Sweden, contractor Strabag Sverige decided to work with Sandvik DT920i and iSURE tunnel management excavation management tool in a recent project they completed for Svensk Känrbränslehandling AB (Swedish Nuclear Fuel and Waste Management). The purpose of the project was to extend the underground laboratory facilities with three transportation tunnels at about 350 metres and a number of experiment niches. Much of the research on the final repository for spent nuclear fuel in Sweden is being done at this specific laboratory on the island of Äspö. This is where different technical solutions are being tested in a real environment on full-scale with Swedish and international experts.

The Strabag contract included blasting, loading, transportation of rock masses, sealing and reinforcement work on two of these areas, with an option for the third tunnel. The excavation volume was about 13 000 m3, going to the depth of 420 meters. Blasting work itself was a part of the research and development of nuclear fuel repository.

Posiva, a Finnish nuclear waste management expert, with the operating contractor Destia Oy, has also chosen a Sandvik DT920i to excavate an underground rock characterization facility, ONKALO that will be extended to the final disposal depth of approximately -400m.  ONKALO facilitates bedrock research and, in addition, also provides an opportunity to develop excavation techniques and final disposal techniques in realistic conditions. Later, the ONKALO facilities can be put into use when building and using the final repository. ONKALO consists of one access tunnel and three shafts: a personnel shaft and two ventilation shafts. The slope of the tunnel is 1:10. It is 5.5 m wide and 6.3 m high. The rock type in the project is medium Gneiss with the strength of 114 kPa.

Intelligent tunneling brings outstanding accuracy

The computer-controlled Sandvik DTi series jumbos are famous for their outstanding accuracy. They come in five different models for excavation of 12 – 231 m2 cross sections, including face drilling, bolt hole drilling and long-hole drilling. The DTi jumbos are designed for automatic use which translates into highest process repeatability and best possible excavation predictability. In addition, the rigs are equipped with Sandvik iSURE tunnel excavation management tool. This combination ensures optimized blasting as per plan, supplying better pull-out, decreased need for scaling, increased rock loadability and smoother collaring in the following round.

Today, thanks to their top-rate usability, the Sandvik DTi series jumbos can be found in nearly every corner of the world. In addition to Finland and Sweden, they have been delivered to South Korea, China, Venezuela, Bhutan, Hong Kong, Australia, Spain, Columbia and Switzerland.

For more information, please contact:

Nina Lehtonen, Marketing Communications, Surface Drilling and Tunneling

Tel. +358 400 534 344 E-mail: nina.lehtonen@sandvik.com

--------------------------------------------------------------------------------------------------------------------------------------------------

Sandvik Group
Sandvik is a global industrial group with advanced products and world-leading positions in selected areas – tools for metal cutting, equipment and tools for the mining and construction industries, stainless materials, special alloys, metallic and ceramic resistance materials as well as process systems. In 2012 the Group had about 49,000 employees and representation in 130 countries, with annual sales of about 99,000 MSEK.

Sandvik Construction
Sandvik Construction is a business area within the Sandvik Group providing solutions for virtually any construction industry application encompassing such diverse businesses as surface rock quarrying, tunneling, excavation, demolition, road building, recycling and civil engineering. The range of products includes rock tools, drilling rigs, breakers, bulk-materials handling and crushing and screening machinery. In 2012 sales amounted to about 9,700 MSEK, with approximately 3,300 employees.

Excavation accuracy, optimized performance and low-risk operation

Sandvik DTi: Promoting continuous improvement in tunneling

In 2008, Sandvik launched new intelligent tunneling jumbos, the Sandvik DTi series, to the first market areas. Ever since, the series has been a great success, fast becoming the industry-leader in optimized performance, outstanding excavation accuracy and low-risk operation in almost every corner of the world.

Despite the successful receipt among the tunneling sites, further development of the DTi series is continuously on-going. Since the launch, the fruits of that work have brought into the machines additional practical features for accurate and fast tunneling such as WLAN remote access, iBOLT systematic bolting and total station navigation. Aspects of work site safety have been also carefully considered in the Sandvik DTi series, and the latest news include, among others, an Access Detection System that stops feed and rotation if a person is entering the working area of the booms.  Other recently introduced features are high frequency RD5 series rock drills for optimized performance, and TIER4 engines.

Access detection decreases risks caused by human errors

The new Access Detection System enhances safe excavation by decreasing risks caused by human actions and errors. The system includes detection sensors on the sides of the jumbo. If a person is recognized in the detection field, boom operations – rotation and feed - will automatically be stopped. In other words, access detection prevents anyone from entering the working area of the booms while they are in operation. If boom operation is automatically stopped, the system must be de-activated with a separate reset by the operator before drilling is released.

In addition to the Access Detection System, the DTi jumbos also feature a manual prevention switch for boom and drilling movements. Safety needs have been considered in the mechanical structure of the jumbo as well, in the form of yellow marking in all access ways, steps, ladders and handles. In addition, the spiral hoses are made of fire-resistant material. All these features greatly improve the work site safety.

RD5 rock drills for optimized performance

Sandvik DTi series jumbos are equipped with new, advanced Sandvik RD5 series high frequency rock drills. The RD5 series features low profile height and a patented stabilizer with an intelligent control system that dampens harmful shockwaves. The simple body structure of the drills along with their modular construction and visual wear indicators guarantee ease of use and maintenance. Built to last, the robust and reliable drills feature only few pressurized seams between functional modules.

With 15 - 20 percent higher penetration rates and significantly longer tool life compared to HLX5*, the robust and reliable RD5 series rock drills offer carefully optimized, cost-effective performance.

Advanced supporting features

The DTi series features a TRH rod handling system, offering an ergonomic and mechanized way of extension rod handling. With its low weight, compact, durable and protected structure and cabin control, it meets the specific needs of any tunneling works. In addition to this, a centralizing rod retainer SCR holds extension rods in place during coupling and uncoupling. It also keeps the rod centralized while clamping.

Intelligent tunneling for outstanding accuracy

The computer-controlled Sandvik DTi series jumbos are famous for their outstanding accuracy. They come in five different models for excavation of 12 – 231 m2 cross sections, including face drilling, bolt hole drilling and long-hole drilling.

The DTi jumbos are designed for automatic use which translates into highest process repeatability and best possible excavation predictability. The user-friendly iDATA control system features full round drilling automatics, one hole drilling automatics and automatic boom positioning according to drill plan. The automatic functions also include boom self-collision detection and hole length control.

The further intelligence features in the DTi jumbos include data collection of production and process information such as round data, cumulative production data and drilling parameters logging that, in turn, help production logistics planning, scheduled maintenance and productivity improvement.

The DTi rigs are equipped with Sandvik iSURE® tunnel excavation management tool. This combination ensures optimized blasting as per plan, supplying better pull-out, decreased need for scaling, increased rock loadability and smoother collaring in the following round.

* 40 % longer tool life for the shank and 17 % for the bits compared with HLX 5 in test conditions.

RD525/520 in brief:

| Hole diameter, drifting | 43 – 64 mm |
| --- | --- |
| Hole diameter, cut hole drilling | 76 – 127 mm |
| Power class | 25/20 kW |
| Percussion rate | 94/74 Hz |
| Max. percussion pressure | 235/220 bar |

For more information, please contact:

Nina Lehtonen, Marketing Communications, Surface Drilling and Tunneling

Tel. +358 400 534 344 E-mail: nina.lehtonen@sandvik.com

--------------------------------------------------------------------------------------------------------------------------------------------------

Sandvik Group
Sandvik is a global industrial group with advanced products and world-leading positions in selected areas – tools for metal cutting, equipment and tools for the mining and construction industries, stainless materials, special alloys, metallic and ceramic resistance materials as well as process systems. In 2012 the Group had about 49,000 employees and representation in 130 countries, with annual sales of about 99,000 MSEK.

Sandvik Construction
Sandvik Construction is a business area within the Sandvik Group providing solutions for virtually any construction industry application encompassing such diverse businesses as surface rock quarrying, tunneling, excavation, demolition, road building, recycling and civil engineering. The range of products includes rock tools, drilling rigs, breakers, bulk-materials handling and crushing and screening machinery. In 2012 sales amounted to about 9,700 MSEK, with approximately 3,300 employees.