FOR IMMEDIATE RELEASE

## May 8, 2012

Headline:  Team of Robbins EPBs rallies at Nanjing Metro

Sub-Headline: Fierce TBM Foursome forges ahead in China’s Mixed Ground

Nearly 750,000 people currently ride the rails daily on two existing metro lines in Nanjing, Jiangsu Province, China.  That number is slated to dramatically increase with the construction of several new metro lines utilizing 40 TBMs, including four Robbins EPBs.   The rail routes have a firm completion deadline of 2014, when they will need to be ready for up to 40,000 visitors attending the Youth Olympic Games in Nanjing.

Robbins provided four 6.5 m (21.4 ft) diameter EPBs with mixed ground cutterheads for two metro lines under construction. The two pairs of EPBs are excavating Line 3 Lot 11 and Line 10 Lot 5, for the China Railway Construction Corporation (CRCC) 13th Engineering Bureau and 23rd Engineering Bureau, respectively.

The two Robbins TBMs for Line 10 were launched in December 2011 and February 2012, while the Line 3 machines were launched in January and March of 2012. “Robbins is a special TBM manufacturer and the quality is good here.  We have used one Robbins TBM previously in Chengdu, and there was very good performance at the Metro Line 2,” said Li QuanShe, Nanjing Line 3 Project Manager for CRCC Bureau 23. At that previous Chengdu jobsite, a Robbins EPB achieved a project record of 129 m (423 ft) in one week through mixed ground.

Ground conditions on both Nanjing lines include soft soil, silty sand, manmade materials, small pebbles, and sandstone.  Shallow cover of 8 to 10 m (26 to 33 ft), a sensitive urban environment, and strict settlement requirements of less than 10 to 20 mm (0.4 to 0.8 in) are requiring customized excavation methods. “The earth is quite soft so we are keeping the thrust force very low (6,000 to 9,000 kN / 1.4 to 2.0 million lb). The operator is also employing continuous monitoring to maintain the proper alignment and earth pressure,” said Jason Xiao, Robbins Project Manager.  Foam additive will also be used to make the ground less sticky and reduce the required torque to excavate the material.

As of May 2012 the Line 10 EPBs have excavated over 600 m and 500 m (1,970 ft and 1,640 ft) of Line 10, respectively.  Advance rates are on the order of 40 mm (1.6 in) per minute, while settlement has stayed below the required limits.  At Line 3, the Robbins machines have excavated over 500 m and 100 m (1,640 m and 330 ft), respectively, with advances topping 60 mm (2.4 in) per minute.

Construction of the 40.2 km (25.0 mi) long Metro Line 3 and the 41.4 km (25.7 mi) long Metro Line 10 is well underway for owner Nanjing Metro Company.  The new subways are part of the municipal government’s extensive plans to improve access across the Yangtze River Basin with up to 17 rail routes totaling 600 km (370 mi) by 2030.

WORD COUNT: 468

Images Attached to Email.  If you need a higher resolution image, please contact Desiree Willis.

Captions for Images:

Image 1: The four Robbins EPBs were designed for mixed ground conditions including soft soils, silty sand, pebbles, and sandstone.

Image 2:  Four 6.5 m (21.4 ft) Robbins EPBs are excavating portions of Nanjing, China’s new Metro Lines 3 and 10.

Image 3:  Workers transport segments for installation at Line 10, where two Robbins EPBs have advanced 600 and 500 m (1,970 ft and 1,640 ft) as of May 2012.

Image 4: The four Robbins EPBs are part of Nanjing, China’s massive metro system upgrade for the 2014 Youth Olympic Games.

Contact Information:

## Brianna Home

#### Marketing Director

### Email: homeb@robbinstbm.com

Direct: 253.872.4484

## Desiree Willis

#### Technical Writer

Email: willisd@robbinstbm.com

Direct: 253.872.4490

##### The Robbins Company

29100 Hall Street

Solon, OH 44139

USA