Bayburt Group chooses Sandvik tunneling jumbos for a high speed train project in Turkey

Şenbay-Özgün joint venture, a part of Bayburt Group of companies, recently purchased seven Sandvik tunneling jumbos for Istanbul – Ankara high speed train relocation project “Dogançay”.The project includes 10 kilometers of tunnel, with 1 400 000 m3 of excavation.

Turkish state railway awarded the Doğançay project to the main contractor Şenbay-Özgün on May 10, 2013.

The new 10 kilometer tunnel is being built in the city of Sakarya, with the purpose to cut down the distance between two major Turkish cities, the capital Ankara and Istanbul. The excavation of 1 400 000 m3 is scheduled to last 180 days, and the project is set to be completed on November 11, 2013.

Bayburt Group purchased seven Sandvik underground drill rigs for the project: five units of Sandvik DD321-40 and two Sandvik DT820s. The excavation in the high speed railway project will be challenging due to fractured rock and weak types such as siltstone, clay stone and mudstone. The Bayburt group chose Sandvik underground drill rigs as they are trouble-free and easy to operate. Another key factor was Sandvik’s high quality service and support network in Turkey.

| Technical specifications DD321-40 DT820 Coverage 8 - 49 m2 12 - 110 m2 Hole diameter 43 - 64 mm 43 - 64 mm Hole length 2 830 – 4 660 mm up to 6 180 mm Booms 2 x SB40 2 x TB90 Feed TF500, 12 ft 2 x TF500, 16 ft Rock drill 2 x RD520, 20 kW 2 x HLX5T, 22 kW Control and operation system THC561, hydraulic THC560, hydraulic Cornering 3 700 mm 4 730 mm Length (with default feed) 12 350 mm 14 900 mm Width (drilling) 2 150 mm 3 000 mm Height (drilling) 3 200 mm 3 600 mm Weight (standard) 22 000 kg 26 500 kg |  |
| --- | --- |

For more information, please contact:

Nina Lehtonen, Marketing Communications, Surface Drilling and Tunneling

Tel. +358 400 534 344 E-mail: nina.lehtonen@sandvik.com

--------------------------------------------------------------------------------------------------------------------------------------------------

Sandvik Group
Sandvik is a global industrial group with advanced products and world-leading positions in selected areas – tools for metal cutting, equipment and tools for the mining and construction industries, stainless materials, special alloys, metallic and ceramic resistance materials as well as process systems. In 2012 the Group had about 49,000 employees and representation in 130 countries, with annual sales of about 99,000 MSEK.

Sandvik Construction
Sandvik Construction is a business area within the Sandvik Group providing solutions for virtually any construction industry application encompassing such diverse businesses as surface rock quarrying, tunneling, excavation, demolition, road building, recycling and civil engineering. The range of products includes rock tools, drilling rigs, breakers, bulk-materials handling and crushing and screening machinery. In 2012 sales amounted to about 9,700 MSEK, with approximately 3,300 employees.